## Slide 1
DON'T TRASH IT.
RECHARGE IT. ⚡
How old EV batteries are getting a sick second life
#SecondLifeBatteries #CleanEnergy #NoWaste
Notes: Yo, what's good everyone! Let's talk about something that's actually lowkey genius — second life batteries.
So here's the deal. Every electric car on the road right now? It's running on a massive battery pack. And when that battery gets too weak to keep the car going — we're talking 70 to 80 percent of its original power left — most people think it's done. Cooked. Time to recycle it, right?
WRONG. That's literally still a ton of energy just sitting there. Imagine your phone at 75 percent — you're not throwing it away, are you? Same energy.
These "retired" EV batteries are getting a whole second life powering things like buildings, solar farms, cell towers, and — this is the wild part — actual AI data centers. We're talking thousands of GPUs running on batteries that came out of someone's old Tesla or Nissan Leaf. That's insane.
This presentation is going to break down how it all works — the science behind why batteries degrade, how they get sorted and rebuilt for round two, where they end up, and why this is literally one of the smartest moves for the planet right now. No cap.
Let's get into it.

## Slide 2
Battery Degradation Overview
70–80%
State of Health
End-of-automotive-life threshold — still viable for stationary storage
8–15 yrs | 150–300k km
Typical EV battery lifespan before second life eligibility
Capacity Fade Mechanisms
SEI layer growth, lithium plating, and active material loss reduce usable capacity over time
Calendar & Cycle Aging
Degradation continues even when idle — cycling and temperature extremes accelerate the process
Second Life Viability
Remaining capacity is insufficient for EV range demands but ideal for stationary energy storage
First Life (EV)
Degradation Zone
Second Life
Notes: Let's start with the fundamentals of why second life batteries exist as an opportunity.
Lithium-ion cells degrade through multiple mechanisms. The solid electrolyte interphase layer grows over time, consuming cyclable lithium. Lithium plating occurs during fast charging or low-temperature operation, creating dendrites that reduce capacity and pose safety risks. Active material particles crack under mechanical stress from repeated expansion and contraction.
The key threshold is 70-80% State of Health. Below this point, an EV loses enough range that it becomes impractical for daily driving. However, 70-80% of a 60-100 kWh pack is still 42-80 kWh — more than enough for stationary applications where energy density and weight are far less critical.
Calendar aging is important to note — batteries degrade even when sitting idle, driven by temperature and state of charge. This means timing of second life deployment matters. The sooner a retired pack enters second life service, the more useful life remains.

## Slide 3: Repurposing Process
1
Collection & Intake
Retired packs received, visual inspection, safety check
2
Testing & Grading
SOH measurement, EIS, capacity/impedance testing
3
Module Disassembly
Pack teardown, cell/module sorting by grade
4
BMS Integration
New BMS design, thermal management, enclosure
5
Deployment & Monitoring
Install in 2nd life application, remote monitoring
Notes: This slide walks through the five-stage repurposing pipeline that retired EV battery packs go through before entering second life service.
Stage 1 — Collection and Intake: Packs are received from OEM take-back programs, dealership networks, or salvage yards. Initial safety screening checks for physical damage, leakage, or thermal event history. Packs with severe damage are routed directly to recycling.
Stage 2 — Testing and Grading: This is the most technically critical step. Electrochemical impedance spectroscopy, capacity tests, and pulse power tests determine each pack's State of Health. Packs are graded into tiers — typically A, B, and C — based on remaining capacity and internal resistance.
Stage 3 — Module Disassembly: Packs are disassembled to the module or cell level. Cells within a module are sorted by matching criteria — primarily capacity and impedance — to ensure balanced strings in the second life pack. This is where cell-to-cell variability becomes a real engineering challenge.
Stage 4 — BMS Integration: A new battery management system is designed for the target application. The duty cycle for stationary storage is fundamentally different from automotive — lower C-rates, different temperature profiles, different safety requirements. Thermal management and enclosure design are also addressed here.
Stage 5 — Deployment and Monitoring: The reconfigured system is installed at the target site with remote monitoring infrastructure. Continuous SOH tracking ensures the system is decommissioned before performance drops below acceptable thresholds.

## Slide 4: Second Life Applications
Grid-Scale Storage
Peak shaving, frequency regulation, and renewable integration at utility scale
Commercial & Industrial
Behind-the-meter storage for demand charge reduction and backup power
Residential Storage
Home energy storage paired with solar PV for self-consumption optimization
Telecom & Off-Grid
Replacing diesel generators at telecom towers and remote installations
Notes: Now let's look at where these second life batteries actually go. There are four primary application categories, each with different technical requirements and economic drivers.
Grid-Scale Storage: This is the largest addressable market. Utilities use second life packs for peak shaving — storing cheap off-peak energy and discharging during expensive peak hours. Frequency regulation is another high-value use case where batteries respond to grid frequency deviations in milliseconds. Second life packs are also paired with wind and solar farms to smooth intermittent generation.
Commercial and Industrial: Behind-the-meter installations help large facilities reduce demand charges, which can represent 30-50% of their electricity bill. These systems also provide backup power during outages, replacing or supplementing diesel generators.
Residential Storage: The economics here are driven by solar self-consumption. A homeowner with rooftop PV can store excess daytime generation for evening use. Second life packs at 30-70% lower cost than new batteries dramatically improve the payback period for home storage systems. Companies like Nissan with xStorage and BMW with their i3 repurposing program are already active in this space.
Telecom and Off-Grid: This is particularly relevant in developing markets where telecom towers rely on diesel generators for backup. Second life batteries can replace diesel entirely, reducing operating costs and emissions. Off-grid communities and remote industrial sites also benefit from affordable energy storage.

## Slide 5: Case Study: Powering AI Data Centers
Crusoe × Redwood Materials
World's largest second-life battery deployment — powering off-grid modular AI data centers at Redwood's Sparks, Nevada campus
12 MW
Solar Generation
63 MWh
Battery Storage
2,000
GPUs Powered
How It Works
20-Acre Solar Array
Generates clean power during daylight hours
Second-Life EV Batteries
Store energy for 24/7 continuous operation after sunset
Crusoe Spark™ Data Center
Modular AI compute with power, cooling & GPU racks integrated
"Reused packs can be deployed at roughly half the cost of new systems, while offering comparable performance in stationary settings."
— Redwood Materials · Pipeline: 1+ GWh deployed, 5 GWh planned · 100+ MW projects in design · Energy cost below grid prices
Notes: This is one of the most exciting real-world applications of second life batteries emerging right now — powering AI data centers.
In June 2025, Crusoe Energy and Redwood Materials unveiled the world's largest second-life battery deployment at Redwood's campus in Sparks, Nevada. The system is a 12 megawatt, 63 megawatt-hour microgrid combining a 20-acre solar array with hundreds of repurposed EV battery packs. It powers Crusoe Spark — a modular, off-grid AI data center containing 2,000 GPUs designed for high-performance AI workloads.
This is significant because AI infrastructure faces a massive power challenge. Goldman Sachs estimates AI will drive a 165% increase in data center power demand by 2030. Traditional grid connections can take years to establish, but this solar-plus-second-life-battery microgrid can be deployed in months.
JB Straubel, the Tesla co-founder who runs Redwood Materials, describes the economics: reused packs deploy at roughly half the cost of new battery systems, while delivering comparable performance for stationary applications. The microgrid is already delivering energy below grid prices.
The scale-up potential is enormous. Redwood processes 20 GWh of batteries annually from about 250,000 EVs — roughly 90% of all lithium-ion batteries recycled in North America. They already have over a gigawatt-hour in their deployment pipeline with 5 GWh more planned, and are designing projects at 100+ megawatts — ten times the size of this initial deployment.
As Crusoe's COO Cully Cavness put it: "In the energy industry, the holy grail has been 24/7 renewable power, but the cost of batteries was too high — until today."

## Slide 6: Technical Challenges
!
Cell Variability
Inconsistent degradation across cells requires advanced sorting and matching algorithms
⚙
BMS Redesign
Second life packs need custom battery management systems for new duty cycles
⚡
Safety Standards
No unified standards for second life certification — UL 1974 is emerging but not universal
◎
RUL Prediction
Remaining useful life estimation requires ML models trained on diverse degradation data
Notes: These are the four major engineering hurdles that the industry needs to overcome for second life batteries to scale.
Cell-to-Cell Variability: Even within the same pack, cells degrade at different rates depending on their position, thermal exposure, and manufacturing variation. When you disassemble a pack, you'll find cells ranging from 65% to 85% SOH. Matching cells with similar characteristics is critical — a string is only as good as its weakest cell. Advanced sorting algorithms using impedance spectroscopy and capacity testing data help optimize matching, but this remains labor-intensive and costly.
BMS Redesign: You can't simply reuse the automotive BMS. The original system was designed for high-power automotive duty cycles with regenerative braking, fast acceleration, and DC fast charging. Stationary storage has fundamentally different requirements — lower C-rates, narrower SOC windows to preserve remaining life, and different thermal management needs. The BMS must also handle the increased cell variability in a second life pack.
Safety Standards: This is arguably the biggest barrier to market adoption. UL 1974 provides a framework for evaluating and repurposing batteries, but it's not universally adopted. IEC 63330 is under development for international standardization. Without clear, widely-accepted standards, insurance companies and regulators remain cautious, limiting deployment in some markets.
Remaining Useful Life Prediction: Accurately predicting how much longer a second life battery will perform is extremely challenging. Degradation is non-linear and depends on future operating conditions that are uncertain. Machine learning models trained on field data from first-life operation are showing promise — companies are using neural networks and physics-informed ML to predict remaining capacity trajectories. This reduces the need for expensive characterization testing and can cut grading costs by up to 40%.

## Slide 7: Outlook & Key Metrics
$4.2B
Projected market size by 2030
30–70%
Cost savings vs. new battery storage
5–10 yr
Additional service life in second use
Key Takeaways
Second life batteries enable circular economy for EV battery packs
UL 1974 and IEC 63330 are defining safety and performance standards
OEMs (BMW, Nissan, Renault) are building vertically integrated repurposing pipelines
AI-driven SOH diagnostics are reducing grading costs by up to 40%
Notes: Let me close with the market outlook and four key takeaways.
The numbers are compelling. The second life battery market is projected to reach 4.2 billion dollars by 2030, driven by the exponential growth in EV sales over the past decade. The first major wave of retired EV packs from vehicles sold in 2015-2020 is now arriving.
The cost advantage is the primary economic driver. Second life battery storage systems cost 30 to 70 percent less than equivalent new battery systems per kilowatt-hour. Even with the costs of testing, grading, disassembly, and BMS redesign, the economics are favorable — especially for applications where energy density is not a constraint.
The additional 5-10 years of service life in second use means a battery originally designed for a 15-year automotive life could deliver 20-25 years of total service. This dramatically improves the lifecycle economics and environmental footprint of EV batteries.
On the takeaways — first, second life batteries are a cornerstone of the circular economy for EVs. They bridge the gap between automotive end-of-life and eventual recycling, extracting maximum value from the embedded energy and materials.
Second, standards are maturing. UL 1974 and IEC 63330 are providing the safety and performance frameworks that insurers and regulators need to feel confident about second life deployments.
Third, OEMs are getting vertically integrated. BMW, Nissan, Renault, and others are building end-to-end repurposing pipelines rather than relying on third parties. This gives them control over quality and creates new revenue streams.
Finally, AI and machine learning are transforming the economics of grading. Automated SOH diagnostics using neural networks can reduce characterization time and cost by up to 40 percent, making the repurposing pipeline more scalable.
Thank you — happy to take questions.