## Slide 1: Second Life Batteries in Electric Vehicles
Repurposing EV Batteries for Stationary Energy Storage: A Technical and Economic Review

## Slide 2
Introduction & Context
The EV Battery Challenge
Global EV sales surpassed 14 million units in 2023, driving exponential growth in lithium-ion battery deployment
EV batteries reach end-of-vehicle-life at 70–80% State of Health (SOH), retaining significant usable capacity
By 2030, an estimated 12 million metric tons of EV batteries will require end-of-life management
Why Second Life?
Direct recycling recovers materials but wastes remaining energy capacity
Second life applications extend useful life by 5–10 years before recycling
Aligns with circular economy principles and EU Battery Regulation (2023/1542)

## Slide 3
What Are Second Life Batteries?
Second life batteries are lithium-ion battery packs retired from electric vehicles that retain 70–80% of original capacity, repurposed for less demanding stationary energy storage applications.
Repurposing Process
Collection and dismantling from retired EVs
State of Health (SOH) testing and grading
Module-level or pack-level reconfiguration
Integration with new BMS for second application
Deployment in stationary storage systems
Key Thresholds
100–80% SOH: First life (in-vehicle use)
80–40% SOH: Second life applications
<40% SOH: Material recycling stage
Repurposing vs. Recycling
Repurposing maximizes value before material recovery
Cascade model: Use → Reuse → Recycle

## Slide 4
Key Applications
Grid-Scale Energy Storage
Peak shaving and load leveling Frequency regulation services Capacity: 1–100 MWh systems
Renewable Energy Integration
Solar and wind power buffering Smoothing intermittent generation Microgrid stabilization
Commercial & Industrial
Behind-the-meter storage Demand charge reduction UPS and backup power systems
Residential & Community
Home energy storage (5–15 kWh) EV charging station buffering Off-grid and rural electrification

## Slide 5
Technical Considerations
SOH Assessment
Electrochemical impedance spectroscopy (EIS)
Capacity fade and resistance growth analysis
Data-driven SOH estimation using ML models
Standardized testing protocols (IEC 62660)
Degradation Modeling
Calendar and cycle aging mechanisms
Semi-empirical and physics-based models
Remaining useful life (RUL) prediction
Temperature and C-rate dependency mapping
Safety & Standards
UL 1974 standard for battery repurposing
Thermal runaway risk mitigation
BMS recalibration requirements
Transportation and handling regulations

## Slide 6
Environmental Impact
Life Cycle Assessment (LCA)
Second life use reduces total lifecycle CO₂ emissions by 25–42% compared to direct recycling
Displaces new battery manufacturing for stationary storage
Reduces demand for critical raw materials: lithium, cobalt, nickel, manganese
Delays hazardous waste generation by 5–10 years per battery pack
Key Metrics
~42 kg CO₂eq/kWh avoided per second life cycle
Up to 70% reduction in cumulative energy demand vs. new storage
Circular Economy Benefits
Extends total battery utilization from ~10 to 15–20 years
Supports EU Battery Regulation Article 59 requirements for repurposing
Creates value retention across multiple product life stages
Resource Conservation
Reduces pressure on mining of lithium and cobalt
Minimizes environmental degradation from extraction
Aligns with UN Sustainable Development Goals (SDG 7, 12, 13)

## Slide 7
Economic Analysis
Market Projections
Global SLB market projected to reach $4.2B by 2030
CAGR of ~25% from 2024–2030
Cost Advantage
SLBs cost 30–60% less than new batteries per kWh
LCOS competitive at $100–150/MWh
Business Models
Battery-as-a-Service (BaaS) leasing
OEM vertical integration (Nissan, BMW, Renault)
Third-party refurbishment startups
Chart: Cost per kWh ($/kWh)
| Grid Storage | Commercial | Residential
New Battery | 280 | 320 | 350
Second Life | 120 | 150 | 180

## Slide 8
Challenges & Research Gaps
1
Standardization
Lack of universal grading standards for retired batteries; heterogeneous pack designs across OEMs complicate module-level reuse
2
Degradation Uncertainty
Limited long-term data on second life degradation trajectories; calendar aging during storage periods remains poorly characterized
3
Liability & Regulation
Unclear product liability frameworks for repurposed batteries; evolving regulatory landscape across jurisdictions
4
Technical Barriers
BMS compatibility and data access challenges; cell-to-cell variability increases with age, complicating system integration

## Slide 9
Conclusion & Future Outlook
Key Takeaways
Second life batteries offer a viable pathway to maximize value from EV battery investments while reducing environmental impact
Cost advantages of 30–60% over new batteries make SLBs economically compelling for stationary storage
Standardization, liability frameworks, and degradation modeling remain critical research priorities
Emerging Research Directions
AI-driven diagnostics: Machine learning for rapid SOH assessment and RUL prediction at scale
Digital battery passports: Blockchain-based lifecycle tracking mandated under EU regulations by 2027
V2G integration: Vehicle-to-grid technology bridging first and second life applications
Design for second life: OEMs incorporating modular, standardized pack architectures for easier repurposing
LFP chemistry shift: Longer cycle life of LiFePO₄ batteries improving second life economics